## Slide 1
LLM Transcribed Voice Controlled Robotic Arm
By Justin Mascarenhas
EEEE685 - Final Project

## Slide 2
Introduction
• Robotic arms are fundamental in automation and manufacturing
• Traditional control methods require specialized knowledge
• Voice control makes robotics accessible to everyone
• This project combines:
  • Speech recognition using LLM transcription
  • Inverse Kinematics for precise positioning
  • Arduino-based servo control
  • Bluetooth wireless communication
Notes: SPEAKER NOTES (1 minute):
- Start by explaining the motivation - robotic arms are everywhere but hard to control
- Voice control democratizes robotics
- Mention the key technologies: LLM for speech-to-text, IK for math, Arduino for hardware
- This project bridges the gap between human intent and robot motion

## Slide 3
Project Overview
Hardware Components
• 3-DOF Robotic Arm (ACEBOTT QD007)
• Arduino Nano (ATmega328P)
• 5× SG90 Servo Motors
• HC-05 Bluetooth Module
• External 5V Power Supply
Software Stack
• PlatformIO / Arduino Framework
• Custom Inverse Kinematics Engine
• Serial & Bluetooth Command Parser
• LLM Speech-to-Text Integration
• Smooth Motion Interpolation
Notes: SPEAKER NOTES (1 minute):
- Walk through the hardware: 5-DOF means 5 degrees of freedom (base rotation, shoulder, elbow, wrist, gripper)
- Arduino Nano is the brain - processes commands and controls servos
- Bluetooth allows wireless control from phone/computer
- Software side: PlatformIO for development, custom IK solver, dual command interfaces

## Slide 4
Implementation : Inverse Kinematics & DH Parameters
• Denavit-Hartenberg (DH) Parameters define arm geometry:
  • L0 = 7.2 cm (Base height to shoulder pivot)
  • L1 = 7.5 cm (Upper arm: shoulder to elbow)
  • L2 = 17.5 cm (Forearm: elbow to end effector)
• 2R Planar Arm Model (Y-Z plane):
  • Uses Law of Cosines for elbow angle
  • Calculates shoulder angle from target position
• Servo Offset Calibration:
  • Shoulder: IK 90° → Servo 125° (+35° offset)
  • Elbow: IK 90° → Servo 75° (-15° offset)
  • Base: Command 90° → Servo 135° (+45° offset)
Notes: SPEAKER NOTES (1.5 minutes):
- DH parameters are standard way to describe robot arm geometry
- L0, L1, L2 are the physical link lengths measured from the arm
- We use a 2R planar model - simplifies 3D problem to 2D (ignoring base rotation)
- Law of Cosines: cos(θ) = (a² + b² - c²) / 2ab
- Key insight: IK calculates LOGICAL angles, but servos need PHYSICAL angles
- Calibration was crucial - each servo has an offset due to mounting position
- Example: When IK says 90°, we write 125° to shoulder servo to get actual 90° position

## Slide 5
Implementation: DH Parameter Table & Servo Mapping
Joint | θ (angle) | d (offset) | a (length) | α (twist)
Base | θ₁ (variable) | L0 = 7.2cm | 0 | 90°
Shoulder | θ₂ (variable) | 0 | L1 = 7.5cm | 0°
Elbow | θ₃ (variable) | 0 | L2 = 17.5cm | 0°
Wrist | θ₄ (variable) | 0 | 0 | 0°
Gripper | θ₅ (variable) | 0 | 0 | 0°
Notes: SPEAKER NOTES (30 seconds):
- This table shows the standard DH parameters
- θ is the joint angle (what we control)
- d is the offset along the z-axis
- a is the link length
- α is the twist angle between joints
- For our 2R planar IK, we mainly use L1 and L2 for the shoulder-elbow calculation

## Slide 6
Achievements
• Complete IK Implementation:
  • Accurate position control using law of cosines with 1cm accuracy
  • Workspace boundary checking (5-30cm Y, 5-25cm Z)
  • Smooth motion interpolation (30 steps per move)
• Dual Command Interface:
  • Serial commands: F10, B5, U3, D2, G15,20, H, P
  • Bluetooth commands: move:forward:10, position:15,20
• Precise Servo Calibration:
  • Pin mapping verified for all 5 servos
  • Offset calibration for accurate positioning
• Consistent Positioning:
  • F5 + B5 returns to exact same position
Notes: SPEAKER NOTES (1 minute):
- The IK engine works! Given a Y,Z position, it calculates the exact servo angles needed
- We have workspace limits to prevent the arm from trying impossible positions
- Two ways to control: direct serial commands for testing, Bluetooth for wireless
- Calibration was a major achievement - each servo had unique offset requirements
- The acid test: move forward 5cm, then back 5cm - arm returns to EXACT same spot
- This proves the IK math is working correctly with the calibrated offsets

## Slide 7
Challenges & Issues Encountered
Technical Challenges
• Servo offset calibration required physical testing
• IK angles vs physical servo angles mismatch
• SoftwareSerial conflicts with PWM pins
• Power supply stability for 5 servos
The Arm and servos have assembly errors which accumulate overtime
Current Limitations
• Voice control integration in progress
• No feedback sensors (open-loop control)
• Limited to 2D planar movements with rotation freedom
• Wrist orientation not included in IK
• Bluetooth range limitations
Notes: SPEAKER NOTES (1 minute):
- Biggest challenge: figuring out servo offsets. IK calculates 90°, but servo needs 125° to actually be at 90° position
- Had to physically test each servo to find correct pin mappings
- Power issues - 5 servos draw significant current, needed external supply
- Current limitations: we're doing open-loop control - no position feedback
- Voice control is the next big integration step

## Slide 8
Future Work
• Voice Control Integration:
  • Connect local LLM service
  Add perception stack
  • Example: "Pick up the red block and place it on the left"
• Hardware Improvements:
  • Add position feedback sensors (encoders/potentiometers)
  • Implement closed-loop control
  • Upgrade to higher torque servos
• Software Enhancements:
  • Full 3D workspace with wrist orientation
  • Path planning and obstacle avoidance
  • Mobile app for intuitive control
• Applications:
  • Educational robotics platform
Notes: SPEAKER NOTES (1 minute):
- The exciting next step is voice control - imagine just telling the robot what to do
- LLM can parse natural language: "move forward a bit" → F5 command
- Hardware upgrades: feedback sensors would enable closed-loop control for higher accuracy
- Full 3D IK would include wrist orientation for more complex tasks
- Real-world applications: help people with disabilities, or teach robotics to students
- The foundation is solid - now we build on it!

## Slide 9
Thank You!
Questions?
EEEE685 - Final Project